# Requirements
- Raspberry Pi Zero[1]
  [1] ZeroW will also work.
- uSD card, 8GB minimum but bigger is better
- DAC hat/phat/bonnet e.g Pimoroni phatdac
- Head unit with AUX input
- USB A to micro USB cable
- 12v to 5v PSU
- Optional
  - case
- For setup
  - PSU
  - Linux computer with gparted installed e.g. raspberry pi[2], PC with live CD/DVD/USB stick
    [2] This can be the same raspberry pi you’re using in the final device but you will need a second uSD card to boot it from.
  - USB uSD card reader
  - USB otg adaptor
  - USB ethernet adaptor[3]
    [3] WiFi may be used instead but is not covered here.
  - Ethernet cable
  - Optional
    - HDMI monitor or TV
    - HDMI adaptor and cable
    - USB hub
    - USB keyboard
    - USB mouse

# One – OS installation
Download and install the latest Raspbian Lite image in the usual way. See https://www.raspberrypi.org/documentation/installation/installing-images/README.md
# Two – Partition Configuration
1. Enable ssh: create an empty file called ssh in the first partition of your uSD card.
2. Connect the card reader and uSD card to your linux computer.
3. Launch gparted. This needs to be done as root or with sudo/gksudo
4. Select the correct device[4]. It should have two small partitions labled “boot” and “rootfs” and a large amount of free space.
  [4] If using a raspberry pi, you want the one appearing as /dev/sd? not /dev/mmcblk0
5. Expand the “rootfs” partition to approximately 4GB.
6. In the free space, create a new FAT32 partition. Use all of the available space. We’ll be using this partition to store our music.
7. Apply changes
8. Exit gparted
9. Remove uSD card
# Three – First Boot and OS Configuration
1. Insert uSD card into pi zero
2. Connect USB otg adaptor
3. Connect monitor, hub, mouse, and keyboard if using.
4. Connect USB ethernet adaptor, and ethernet cable
5. Boot your pi zero
6. Login to your pi
7. Update package lists:
  sudo apt update
8. Upgrade software:
  sudo apt upgrade
9. Run
  sudo raspi-config
10. Under boot options set wait for network to no
11. Optionally change hostname
12. Exit raspi-config
# Four – Configure Music Library Storage
1. Create a mount point for the music library storage: sudo mkdir /music
2. Open /etc/fstab in your favourite editor[5] e.g. sudo vi /etc/fstab
  [5] Yeah, I’m old school. Change vi to your favourite.
3. Add a new entry as follows:
  /dev/mmcblk0p3	/music	vfat	ro,umask=000	0	0
4. Save and close /etc/fstab
5. Mount music storage as read/write:
  sudo mount -o rw /music
6. Create playlists directory:
  mkdir /music/playlists
7. Unmount music storage:
  sudo umount /music

# Five – USB Mass Storage Gadget
1. Open /boot/config.txt in your favourite editor, this will need sudo.
2. Add a new line at the bottom of the file:
  dtoverlay=dwc2
3. Save and close /boot/config.txt
4. Open /etc/rc.local in your favourite editor, this will need sudo.
5. Above “exit 0” add the following:
  modprobe g_mass_storage removable=1 file=/dev/mmcblk0p3 &
6. Save and close /etc/rc.local
# Six – Sound Card
1. Follow the manufacturer’s instructions.
2. If using Pimoroni’s phat DAC:
  curl -sS https://get.pimoroni.com/phatdac | bash
# Seven – Install and Configure MPD
1. Install mpd and mpc:
  sudo apt install mpd mpc
2. Stop mpd:
  sudo systemctl stop mpd
3. Backup mpd.conf:
  sudo cp /etc/mpd.conf /etc/mpd.conf.bak
4. Open /etc/mpd.conf in your favourite editor, this will need sudo.
5. Find the line that starts with “music_directory” or “#music_directory”. Change it to:
  music_directory	“/music”
6. Find the line that starts with “playlist_directory” or “#playlist_directory”. Change it to:
  playlist_directory	“/music/playlists”
7. Find the line that starts with “log_file” or “#log_file”. Change it to:
  log_file	“/var/log/mpd.log”
8. Find the line that starts with “auto_update” or “#auto_update”. Change it to:
  auto_update	“no”
9. Find the line that starts with “replaygain” or “#replaygain”. Change it to:
  replaygain	“auto”
10. Find the line that starts with “volume_normalization” or “#volume_normalization”. Change it to:
  volume_normalization	“yes”
11. Restart mpd:
  sudo systemctl start mpd

# Eight – Install MPD Script
1. Download initmpd.sh
2. Move or copy it to /home/pi
3. Ensure it has execute permission:
  chmod +x initmpd.sh
4. Open /etc/rc.local in your favourite editor, this will need sudo.
5. Above “exit 0” but below “modprobe ...” add the following:
  /home/pi/initmpd.sh &
6. Save and close /etc/rc.local
# Nine – Change to Read Only Root
See https://learn.adafruit.com/read-only-raspberry-pi for full information.
1. Download the setup script:
  wget https://raw.githubusercontent.com/adafruit/Raspberry-Pi-Installer-Scripts/master/read-only-fs.sh
2. Run it:
  sudo bash read-only-fs.sh
3. Shutdown your pi:
  sudo poweroff
# Ten – Add Music
1. Disconnect everything from your pi
2. Connect a micro USB cable to the data (inner) port of the pi zero
3. Connect the cable to your PC. The pi will boot and appear as a USB storage drive.
4. Copy music files to this drive
5. Create an empty file called “update” or “update.txt” in the top level directory of the USB drive. This will trigger an update of the mpd database and playlist on next boot.
6. Safely remove and disconnect the pi from the PC.
7. Reboot the pi to run the update. This will take a while[6], how long depends on how much music you have.
  [6] You can monitor this via ssh or wait for the zero to reboot and start playing.