This was built to fulfil a need I had for an in-car music player.

It had to meet the following requirements:
- No modifications to the car, use only existing connections
- Small, easy to hide
- Low power
- Connect to the factory head unit’s AUX in
- Start playing when powered
- Play tracks randomly from all installed music
- Support at least .mp3 format
- Avoid driver distraction:
  - No display
  - No additional controls
- Survive in a hostile power environment with minimal chance of data corruption
- Easy to add/remove music and update any playlist/database

The solution I decided on was a Raspberry Pi Zero, a Pimoroni pHAT DAC, a large capacity uSD card, raspbian stretch lite, mpd, and mpc. All running with a read only filesystem.

Music installation is handled by running the pi zero as a USB mass storage gadget.